###### isc Silicon NPN Power Transistor                  2N3773

###### DESCRIPTION

·Excellent Safe Operating Area

·High DC Current Gain-hFE=15(Min)@IC = 8A

·Low Saturation Voltage-

: VCE(sat)= 1.4V(Max)@ IC = 8A

·Complement to Type 2N6609

APPLICATIONS

·Designed for high power audio ,disk head positioners and

other linear applications, which can also be used in power

switching circuits such as relay or solenoid drivers, DC-DC

converters or inverters.

ABSOLUTE MAXIMUM RATINGS(Ta=25℃)

| SYMBOL | PARAMETER | VALUE | UNIT |
| --- | --- | --- | --- |
| VCBO | Collector-Base Voltage | 160 | V |
| VCEX | Collector-Emitter Voltage | 160 | V |
| VCEO | Collector-Emitter Voltage | 140 | V |
| VEBO | Emitter-Base Voltage | 7 | V |
| IC | Collector Current-Continuous | 16 | A |
| ICP | Collector Current-Peak | 30 | A |
| IB | Base Current-Continuous | 4 | A |
| IBP | Base Current-Peak | 15 | A |
| PC | Collector Power Dissipation @TC=25℃ | 150 | W |
| TJ | Junction Temperature | 150 | ℃ |
| Tstg | Storage Temperature | -65~150 | ℃ |

THERMAL CHARACTERISTICS

| SYMBOL | PARAMETER | MAX | UNIT |
| --- | --- | --- | --- |
| Rth j-c | Thermal Resistance,Junction to Case | 1.17 | ℃/W |

###### SPTECH Silicon NPN Power Transistor          2N3773

ELECTRICAL CHARACTERISTICS

TC=25℃ unless otherwise specified

| SYMBOL | PARAMETER | CONDITIONS | MIN | MAX | UNIT |
| --- | --- | --- | --- | --- | --- |
| VCEO(SUS) | Collector-Emitter Sustaining Voltage | IC=50mA ; IB=0 | 140 |  | V |
| VCEX(SUS) | Collector-Emitter Sustaining Voltage | IC=100mA ; VBE(off)= 1.5V; RBE=100Ω | 160 |  | V |
| VCER(SUS) | Collector-Emitter Sustaining Voltage | IC=200mA ; RBE=100Ω | 150 |  | V |
| VCE(sat)-1 | Collector-Emitter Saturation Voltage | IC= 8A; IB= 0.8A |  | 1.4 | V |
| VCE(sat)-2 | Collector-Emitter Saturation Voltage | IC= 16A; IB= 3.2A |  | 4.0 | V |
| VBE(on) | Base-Emitter On Voltage | IC= 8A ; VCE= 4V |  | 2.2 | V |
| ICEO | Collector Cutoff Current | VCE= 120V; IB=0 |  | 10 | mA |
| IEBO | Emitter Cutoff Current | VEB= 7.0V; IC=0 |  | 5 | mA |
| hFE-1 | DC Current Gain | IC= 8A ; VCE= 4V | 15 | 60 |  |
| hFE-3 | DC Current Gain | IC= 16A ; VCE= 4V | 5 |  |  |
| Is/b | Second Breakdown Collector Current with Base Forward Biased | VCE= 100V,t= 1.0s,Nonrepetitive | 1.5 |  | A |